## Slide 4: Vapor cycle refrigerator

## Slide 9: T-S diagram

## Slide 14
Back side
Front side

## Slide 15: Air-conditioner (AC)

## Slide 20
For Cooling the Room (Forced Convection): The Blower Fan forces the cooled air out of the unit and into the room. This movement of air carries the coldness (or, more accurately, the absence of heat) to all parts of the room, lowering the overall temperature. This is the primary way the air conditioner cools the space.
At the Evaporator Coil: The fan forces the warm room air to move across the cold coil, which is a form of forced convection.
At the Condenser Coil: In the outdoor unit, the Condenser Fan forces air across the hot condenser coil to carry the rejected heat away into the atmosphere.

## Slide 22: Engineering Problem on Rankine Cycle

## Slide 23
In a steam power plant operating on the Rankine cycle, steam enters the turbine at 4 MPa, 400 oC (Super heated vapor region) and exits at a pressure of 15 kPa. Then it enters the condenser and exits as saturated water. Next, a pump feeds back the water to the boiler.
Draw the entire rankine cycle by marking the processes neatly.
Determine the heat supplied to the working fluid in the cycle.
Provided the enthalpy at the entrance of the condenser as 2192.5 kJ/Kg, find the work output of Turbine
From steam table
Enthalpy h =3214.5 kJ/Kg at 400C, 4MPa (at inlet of turbine)
Entropy h= 6.771 KJ/KgK at 400 C, 4 MPa (at inlet of turbine)
Entropy of saturated vapor (on saturated vapor line) at 15 kPa = 8.007 kJ/KgK
Enthalpy of saturated liquid (on saturated liquid line) at 15 kPa = 225.8 kJ/Kg
Specific volume of liquid at the entrance of pump at 15 kPa = 0.001014 m3/Kg

## Slide 24
In a steam power plant operating on the Rankine cycle, steam enters the turbine at 4 MPa, 400 oC (Super heated vapor region) and exits at a pressure of 15 kPa. Then it enters the condenser and exits as saturated water. Next, a pump feeds back the water to the boiler.
Determine the heat supplied to the working fluid in the cycle.
Provided the enthalpy at the entrance of the condenser as 2192.5 kJ/Kg, find the work output of Turbine
From steam table
Enthalpy h =3214.5 kJ/Kg at 400 C
Entropy h= 6.771 Kj/KgK at 400 C (at inlet of turbine)
Entropy of saturated vapor (on saturated vapor line) at 15 kPa = 8.007 kJ/KgK
Enthalpy of saturated liquid (on saturated liquid line) at 15 kPa = 225.8 kJ/Kg
Specific volume of liquid at the entrance of pump at 15 kPa = 0.001014 m3/Kg

## Slide 25
In a steam power plant operating on the Rankine cycle, steam enters the turbine at 4 MPa, 400 oC (Super heated vapor region) and exits at a pressure of 15 kPa. Then it enters the condenser and exits as saturated water. Next, a pump feeds back the water to the boiler.
Determine the heat supplied to the working fluid in the cycle.
Provided the enthalpy at the entrance of the condenser as 2192.5 kJ/Kg, find the work output of Turbine
From steam table
Enthalpy h =3214.5 kJ/Kg at 400 C
Entropy h= 6.771 Kj/KgK at 400 C (at inlet of turbine)
Entropy of saturated vapor (on saturated vapor line) at 15 kPa = 8.007 kJ/KgK
Enthalpy of saturated liquid (on saturated liquid line) at 15 kPa = 225.8 kJ/Kg
Specific volume of liquid at the entrance of pump at 15 kPa = 0.001014 m3/Kg

## Slide 26
In a steam power plant operating on the Rankine cycle, steam enters the turbine at 4 MPa, 400 oC (Super heated vapor region) and exits at a pressure of 15 kPa. Then it enters the condenser and exits as saturated water. Next, a pump feeds back the water to the boiler.
Determine the heat supplied to the working fluid in the cycle.
Provided the enthalpy at the entrance of the condenser as 2192.5 kJ/Kg, find the work output of Turbine
From steam table
Enthalpy h =3214.5 kJ/Kg at 400 C
Entropy h= 6.771 Kj/KgK at 400 C (at inlet of turbine)
Entropy of saturated vapor (on saturated vapor line) at 15 kPa = 8.007 kJ/KgK
Enthalpy of saturated liquid (on saturated liquid line) at 15 kPa = 225.8 kJ/Kg
Specific volume of liquid at the entrance of pump at 15 kPa = 0.001014 m3/Kg

## Slide 30: Engineering Problem on Vapor Cycle

## Slide 31
In a vapour compression refrigeration cycle working with refrigerant R-134A, the evaporator and condenser temperatures are -5 C and 30 C respectively. Draw the T-S diagram of a vapor compression refrigerator cycle
Determine
Compression work
Refrigerating effect
Heat rejected in the condenser
COP
From the data sheet of R-134 A, following information are provided
Enthalpy at the inlet of compressor at -5C = 395.9 kJ/Kg
Enthalpy at the inlet of condenser at 30C and 771 kPa = 420.8 kJ/Kg
Enthalpy after throttling and at the inlet of evaporator = 241.8 kJ/Kg

## Slide 32
In a vapour compression refrigeration cycle working with refrigerant R-134A, the evaporator and condenser temperatures are -5 C and 30 C respectively. The process follows the T-S diagram shown
Determine
Compression work
Refrigerating effect
Heat rejected in the condenser
COP
From the data sheet of R-134 A, following information are provided
Enthalpy at the inlet of compressor at -5C = 395.9 kJ/Kg
Enthalpy at the inlet of condenser at 30C and 771 kPa = 420.8 kJ/Kg
Enthalpy after throttling and at the inlet of evaporator = 241.8 kJ/Kg

## Slide 33
In a vapour compression refrigeration cycle working with refrigerant R-134A, the evaporator and condenser temperatures are -5 C and 30 C respectively. The process follows the T-S diagram shown
Determine
Compression work
Refrigerating effect (QL)
Heat rejected in the condenser
COP of refrigerator
From the data sheet of R-134 A, following information are provided
Enthalpy at the inlet of compressor at -5C = 395.9 kJ/Kg
Enthalpy at the inlet of condenser at 30C and 771 kPa = 420.8 kJ/Kg
Enthalpy after throttling and at the inlet of evaporator = 241.8 kJ/Kg

## Slide 35
Tutorial 5
Second Law

## Slide 36: Gas Turbines and Engines

## Slide 39: Convert P-V diagram of Carnot Cycle to T-S diagram also calculate efficiency using T-S diagram
P
V
isothermal
adiabatic
isothermal
adiabatic
Qin
Qout
Q=0
Q=0
1
2
3
4
Thot
Tcold
T
S
1
2
4
3

## Slide 41
P
V
1
2
3
4
1 to 2 to 3 to 4 to 1
adiabatic
adiabatic

## Slide 42
P
V
1
2
3
4
1 to 2 to 3 to 4 to 1
adiabatic
adiabatic
1 to 2
T
S
1
2

## Slide 43
P
V
1
2
3
4
1 to 2 to 3 to 4 to 1
adiabatic
adiabatic
2 to 3
T
S
1
2
3

## Slide 44
P
V
1
2
3
4
1 to 2 to 3 to 4 to 1
adiabatic
adiabatic
3 to 4
T
S
1
2
3
4

## Slide 45
P
V
1
2
3
4
1 to 2 to 3 to 4 to 1
adiabatic
adiabatic
3 to 4
T
S
1
2
3
4
Using

## Slide 46
P
V
1
2
3
4
1 to 2 to 3 to 4 to 1
adiabatic
adiabatic
3 to 4
T
S
1
2
3
4

## Slide 47
P
V
1
2
3
4
1 to 2 to 3 to 4 to 1
adiabatic
adiabatic
3 to 4
T
S
1
2
3
4

## Slide 48
P
V
1
2
3
4
1 to 2 to 3 to 4 to 1
adiabatic
adiabatic
3 to 4
T
S
1
2
3
4

## Slide 49
P
V
1
2
3
4
1 to 2 to 3 to 4 to 1
adiabatic
adiabatic
4 to 1
T
S
1
2
3
4

## Slide 50: Gas Turbines and Engines

## Slide 64
Applications of Phase Transition’s
Vapor-Liquid
Liquid-Vapor
1. Thermal Power Plant
2. Refrigerator
3. Air Conditions
4. Gas Turbine: Power generation
5. Aircraft Gas Turbine , Propeller, Jet Engines