## Slide 1
Season 2, Lecture 23 (S2,L23):
Chemical Potential and Gibbs Duhem relations
Tutorial 6
MSE Answer sheet display

## Slide 2: Mid Sem Exam Solutions with step wise marks

## Slide 3
A DC electrical motor is used to operate a hoist mechanism (which does lifting of objects) in a crane. The motor is supplied with 300 V and 10 Ampere from a DC source for a period of 2 min. The torque provided by the motor to the hoist shaft is 250 Nm at 50 rpm. The hoist mechanism lifts a mass of 2500 Kg through a height of 5m. Calculate the work interaction for the DC source, motor, hoist and the mass

## Slide 4
2 Marks

## Slide 5
2 Marks

## Slide 6
Air and N2 are contained in an insulated piston cylinder apparatus as shown in the figure. The thin rigid wall that separates the two chambers is perfectly thermally conducting. Initially, the air is at 500kPa and 473K and N2 is at 1500 kPa and they each occupy 0.01 m3. The air is now compressed slowly till the pressure of N2 reaches 1580 kPa. Determine the work and heat interaction for the air and its final temperature. For air and N2, pv = 288T, CV=742 J/Kg K, where p is in N/m2, v is in m3/Kg and T is in K. Neglect any internal energy changes in the partition wall.
4 marks
Given
pv = 288T, CV=742 J/Kg K

## Slide 7
1 Mark

## Slide 8
1 Mark

## Slide 9
1 Mark
1 Mark

## Slide 10
Tank A and a piston-cylinder arrangement B are connected through pipes as shown. The piston is frictionless. Tank A contains Nitrogen at 300 kPa and its volume is 0.4 m3. It requires 150 kPa to lift the piston. As the connecting valve opens, Nitrogen flows into the piston – cylinder arrangement B and attains a steady state after some time. What is the final pressure and work interaction for Nitrogen if the initial and final states are related by pV=C, where p and V represent pressure and volume of the gas and C represents a constant
4 Marks
Marks 2
Marks 2

## Slide 11
A heat engine operates between a hot reservoir at 500 K and a cold reservoir at 300 K. It absorbs 3500 J and rejects 2500 J of heat. Calculate the work done, efficiency and the maximum possible efficiency. 4 Marks
Marks 2
Marks 2

## Slide 12
A sheet of steel 1.5 mm thick has nitrogen atmospheres on both sides at 1200oC and is permitted to achieve a steady state diffusion condition. The diffusion coefficient for Nitrogen in steel at this temperature is 6 X 10-11 m2/s, and the diffusion flux is found to be 1.2 X 10-7 Kg/m2.s. Also it is known that the concentration of Nitrogen in the steel at the high pressure side is 4 Kg/m3. How far into the sheet from this high-pressure side will the concentration be 2 Kg/m3(for convenience choose starting position as x=0)? Assume a linear concentration profile.
4 marks

## Slide 13: Last 3 Questions solutions already available in Lecture ppt’s

## Slide 14
Name | L21 | L22 | L23 | L24 |  |  |  |  |  |  |  |  | 
"2201ph34_dolly" <2201ph34_dolly@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Adhila Aslam" <2201ph01_adhila@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Aditi Baghel" <2201ph31_aditi@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Aditya Kumar" <2201ph02_aditya@iitp.ac.in>; | a | a | p | P |  |  |  |  |  |  |  |  | 
"Aditya Singh" <2201ph03_aditya@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Animesh Sharma" <2201ph05_animesh@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Arun Mishra" <2201ph06_arun@iitp.ac.in>; | a | p | p | P |  |  |  |  |  |  |  |  | 
"Aryan Raj" <2201ph32_aryan@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Boda Vishnuwardhan" <2201ph08_boda@iitp.ac.in>; | p | p | a | P |  |  |  |  |  |  |  |  | 
"Chanchal Tolani" <2201ph09_chanchal@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Gaurav Verma" <2201ph10_gaurav@iitp.ac.in>; | a | p | p | A |  |  |  |  |  |  |  |  | 

## Slide 15
Name | L21 | L22 | L23 |  |  |  |  |  |  |  |  |  | 
"Gourav Jha" <2201ph11_gourav@iitp.ac.in>; | p | p | P |  | P |  |  |  |  |  |  |  | 
"Gurinder Dhillon" <2201ph12_gurinder@iitp.ac.in>; | p | p | p | ch | P |  |  |  |  |  |  |  | 
"Harsh Joshi" <2201ph13_harsh@iitp.ac.in>; | p | p | p |  | P |  |  |  |  |  |  |  | 
"Himanshu Patel" <2201ph35_himanshu@iitp.ac.in>; | m | m | p | ch | A |  |  |  |  |  |  |  | 
"Khushal Yadav" <2201ph14_khushal@iitp.ac.in>; | a | p | p |  | P |  |  |  |  |  |  |  | 
"Krishnakant Chourey" <2201ph15_krishnakant@iitp.ac.in>; | p | a | p |  | A |  |  |  |  |  |  |  | 
"Manas Gupta" <2201ph16_manas@iitp.ac.in>; | p | a | p |  | P |  |  |  |  |  |  |  | 
"Mohit Saini" <2201ph17_mohit@iitp.ac.in>; | p | a | p |  | P |  |  |  |  |  |  |  | 
"Mude Naik" <2201ph18_mude@iitp.ac.in>; | P | p | a |  | P |  |  |  |  |  |  |  | 
"Murari Kumar" <2201ph19_murari@iitp.ac.in>; | p | p | p |  | A |  |  |  |  |  |  |  | 
"Nishant Yadav" <2201ph20_nishant@iitp.ac.in>; | p | p | a |  | P |  |  |  |  |  |  |  | 
"Pranitha Moluguri" <2201ph21_pranitha@iitp.ac.in>; | p | p | p |  | P |  |  |  |  |  |  |  | 

## Slide 16
Name | L21 | L22 | L23 |  |  |  |  |  |  |  |  |  | 
"Premanandh Sigamala" <2201ph22_premanandh@iitp.ac.in>; | a | p | a | P |  |  |  |  |  |  |  |  | 
"Ruchi Thakur" <2201ph23_ruchi@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Satyam Sahoo" <2201ph25_satyam@iitp.ac.in>; | p | p | p |  |  |  |  |  |  |  |  |  | 
"Satyam Shandilya" <2201ph24_satyam@iitp.ac.in>; | a | a | p | P |  |  |  |  |  |  |  |  | 
"Shyam Hembram" <2201ph26_shyam@iitp.ac.in>; “ | p | p | p | P |  |  |  |  |  |  |  |  | 
Sougata Saha" <2201ph27_sougata@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Sumit Rajpoot" <2201ph28_sumit@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
"Suprajit Dewanji" <2201ph29_suprajit@iitp.ac.in>; | p | p | p | P |  |  |  |  |  |  |  |  | 
Attendance: 75% mandatory

## Slide 17: Introduction to Thermodynamics Functions and Maxwell’s relations

## Slide 18: Combining First Law and Entropy

## Slide 20
Conjugate Variables

## Slide 21
We need to conduct experiment at different Entropy and
find Temperature in those conditions
Cumbersome

## Slide 22: Similarly

## Slide 23
We need to conduct experiment at different volumes and
find Pressures in those conditions
Cumbersome

## Slide 25
Now, we define new thermodynamic functions
which depend on T and P, first mathematically
using “Legendre Transformations”
These new Thermodynamic functions turns out to be Gibbs Free Energy G

## Slide 26: Legendre Transformation

## Slide 27: Legendre Transformation

## Slide 29
Thermodynamic Functions

## Slide 31
Maxwell’s Relations
In Thermal Physics
Condition for an Exact differential

## Slide 32
Maxwell’s Relations
In Thermal Physics

## Slide 34
N
N+1

## Slide 35
N
N+1
Chemical Potential

## Slide 36
N

## Slide 37
New variable “N”

## Slide 42
Can we write like
?
Answer is we cannot

## Slide 43
Extensive and Intensive variables
3 pairs of variables we formed
T
S
Conjugate variables
P
V
Extensive variable (depends on quantity of the substance)
Intensive
variables

## Slide 44
At least one extensive variable was present

## Slide 46
Can we write like
?
All are intensive variables
System specification is incomplete

## Slide 47
We cannot define such Thermodynamic function
Gibbs -Duhem relation

## Slide 49
Using Gibbs Duhem relation we could find an absolute value of U

## Slide 50
Thermal energy
Mechanical energy
chemical energy

## Slide 51
Finding other thermodynamic functions using this relation

## Slide 56
We are interested in the thermodynamic properties of a strip of rubber as it is stretched (see below). Consider n moles of pure ethylene propylene rubber (EPR) that has an unstretched length z0.
If it is stretched by applying a force F, it will obtain an equilibrium length z, given by:
f = kT (z–z0 )
where k is a positive constant.
The heat capacity of unstretched EPR is given by:
Cz = (du/dT)z =n(a+bT) where a and b are constants
Come up with fundamental property relations for dU and dF for this system, where F is the Helmholtz energy ( F= U –TS) .
(b) Develop an expression that relates the change in entropy to the changes in temperature and length, use S(T,z) for calculation
(c) Develop an expression that relates the change in internal energy to the changes in temperature and length. For U = U(T, z), find dU.
(d) Consider the relative energetic and entropic contributions to the isothermal extension of EPR.
The energetic force (the component of the force that, on isothermal extension of the rubber,
increases the internal energy) is given by:
fU= (dU/dz)T
while the entropic force is given by:
fS = –T (dS/dz)T
Come up with expressions for fU and fs for EPR.
(e) If the change from the unstretched state to the stretched state above occurred adiabatically, would the temperature of the EPR go up, stay the same, or go down? Explain.
m total
mass

## Slide 57
We are interested in the thermodynamic properties of a strip of rubber as it is stretched (see below). Consider n moles of pure ethylene propylene rubber (EPR) that has an unstretched length z0.
If it is stretched by applying a force F, it will obtain an equilibrium length z, given by:
f = kT (z–z0 )
where k is a positive constant.
The heat capacity of unstretched EPR is given by:
Cz = (du/dT)z =n(a+bT) where a and b are constants
Come up with fundamental property relations for dU and dF for this system, where F is the Helmholtz energy ( F= U –TS) .
m total
mass

## Slide 58
We are interested in the thermodynamic properties of a strip of rubber as it is stretched (see below). Consider n moles of pure ethylene propylene rubber (EPR) that has an unstretched length z0.
If it is stretched by applying a force F, it will obtain an equilibrium length z, given by:
f = kT (z–z0 )
where k is a positive constant.
The heat capacity of unstretched EPR is given by:
Cz = (du/dT)z =n(a+bT) where a and b are constants
Come up with fundamental property relations for dU and dF for this system, where F is the Helmholtz energy ( F= U –TS) .
(b) Develop an expression that relates the change in entropy to the changes in temperature and length, use S(T,z) for calculation
m total
mass

## Slide 59
We are interested in the thermodynamic properties of a strip of rubber as it is stretched (see below). Consider n moles of pure ethylene propylene rubber (EPR) that has an unstretched length z0.
If it is stretched by applying a force F, it will obtain an equilibrium length z, given by:
f = kT (z–z0 )
where k is a positive constant.
The heat capacity of unstretched EPR is given by:
Cz = (du/dT)z =n(a+bT) where a and b are constants
Come up with fundamental property relations for dU and dF for this system, where F is the Helmholtz energy ( F= U –TS) .
(b) Develop an expression that relates the change in entropy to the changes in temperature and length, use S(T,z) for calculation
(c) Develop an expression that relates the change in internal energy to the changes in temperature and length. For U = U(T, z), find dU.
(d) Consider the relative energetic and entropic contributions to the isothermal extension of EPR.
The energetic force (the component of the force that, on isothermal extension of the rubber,
increases the internal energy) is given by:
fU= (dU/dz)T
while the entropic force is given by:
fS = –T (dS/dz)T
Come up with expressions for fU and fs for EPR.
m total
mass

## Slide 65
Using Gibbs Duhem relations find thermodynamic functions
U, H, F and G